## Slide 1: Algorithm For Model Building Example
Tapajyoti Ghosh

## Slide 2: Recap
Input of process data
Input of Economic Data/tables
Matching of Flows and economic sectors with NAICS codes.
Disaggregation calculations.
SPA results.

## Slide 3: Model building
Reading the SPA results.
380
0.000038 380 zero order 0.002765
0.251643 22----248----380 second order 18.501296
0.169661 22----380 first order 12.473812
0.092499 248----380 first order 6.800746
0.088462 198----380 first order 6.503932
0.053039 249----380 first order 3.899574
0.049817 1----198----380 second order 3.662681
0.037676 282----198----380 second order 2.770036
0.034943 22----249----380 second order 2.569091
0.017101 22----1----198----380 third order 1.257307
0.016643 22----248----248----380 third order 1.223651
0.016580 280----198----380 second order 1.219028
0.016203 245----249----380 second order 1.191271
0.014824 22----198----380 second order 1.089865
0.008238 198----198----380 second order 0.605669
0.007716 241----248----380 second order 0.567312
0.007104 280----249----380 second order 0.522280

## Slide 4
The basic idea is that we are going to create a matrix based on the information obtained from the previous slide.
The information for filling up the matrices will come from the database search.
The problem has been reduced to a dual scale type to make it easier for the first version of this software and for this project. So we will just have a process equipment scale(which is the finest sale and the one for which you already entered data for) and the next one is the database/value chain/life cycle scale which we will search the information for. Currently, we are not going to economy.

## Slide 5
Step 1 : Model 380. 380 by default goes to equipment scale. (finest scale).
Step 2 : Model 22----248----380 .
Step 3 : We read from the right side. Now 248 has a NAICS code. The NAICS code also exists in the flow inputs that we gave at the first step. Search for the information in the data entered. And…..Input that in. …. 248----380
Step 4: Any information that goes in the row and column with 380 label will come from the process data that we have entered. Other information will come from the life cycle database search.
Step 5 : The diagonal elements get filled by the reference flow values (output) values from the database search.
Step 6: A unit checks should be there so that units going in every row is consistent. So the value that we imported from the equipment scale info and searched from the database should have same units.

## Slide 6
Step 7: 22----248. Now we need to model this one. This information is not there in the process data that we have entered. So this is going to be searched from the database.
Step 8: So we search for this link in the database and then read the number and input it in….
Step 9: 22----380 . It comes from the process data that we have already entered. No need for increasing size of matrix.
Step 10: 248----380. Check the cell. If value is already there, ignore this step.
Step 11: 198----380. New number/activity comes in. matrix size increases. Value obtained from process data that we entered after NAICS code search.
Step 12: Lower Diagonals are always 0.
Continue on……

## Slide 7
Step 13: Uncertainty data needs to be inputted along with every step (of increase of the size of the matrix or data entry) which I have omitted right now. This data needs to be entered by the user because currently we have don’t have any database with the data available.
Step 14: Complexity data also needs to be entered in terms of price/granularity along with every step. (of increase of the size of the matrix or data entry). Also needs to be entered by the user.
Step 15: A calculation in the background needs to happen for every step of the SPA and two parameters will be displayed as the model generation algorithm proceeds which will determine the stop criteria. These parameters will have some bounds which needs to be entered by the user or specified by default.
Step 16: Additional explorations
Step 17: As we create the main matrix, another matrix/vector with the environmental emissions also needs to be created with process equipment entered data as well as data from searching the database. For example…