## Slide 1: Example for Interface
Tapajyoti Ghosh

## Slide 2: Initial Inputs for the algorithm
Process Level information
For now we consider a one output scenario:
Entry from user –
Process name
NAICS code for process
Process Output – (in some physical units)
Process Output Price – ($)
Process Inputs (n) – n is variable, n number of inputs. (in some physical
units)
Process Input prices (n) - $
Process Input Flow NAICS codes (n)
process Environmental impact - (in some physical units)

## Slide 3: Initial Inputs for the algorithm
Economy model Entry
The user need to enter economy model use and make matrices. These matrices may be available to the user in csv/excel files and they can load them. Alternatively, the interface will have some loaded default matrices that the user can use.
The economy model is a set of three matrices – make (V) [mxm], use (U)[mxm] , final demand (F)[m x1] and environmental (B)[1x m]. All these matrices are available as excel files as well as .m files currently. (m is the size of the model)
Every row and column of these matrices have their NAICS codes again available as excel/csv files.
Once we have all this data, the algorithm proceeds.

## Slide 4: Algorithm
Search the process NAICS code in the economy model NAICS codes list.
If not found – Rebuild V matrix with a new sector. The process output multiplied with price and scale to one year goes to the [m+1, m+1] cell of the V matrix.
Rebuild U matrix by adding process input values multiplied with price and scaled to one year in the [m+1]th column of the use matrix by matching NAICS input flow codes with NAICS economy model codes.
I will help you with these calculations and explain them in more details over our hangout meeting next week.
Similar changes to F and B matrix. Add values to m+1th cell from process level information.

## Slide 5: Algorithm
Search the process NAICS code in the economy model NAICS codes list.
If found – Rebuild V matrix with a new sector. The process output multiplied with price and scale to one year goes to the [m+1, m+1] cell of the V matrix. Additionally subtract the process output multiplied with price and scale to one year from the corresponding cell whose NAICS code matched with the process. There are easy formulas that do that. All we need is a simple match logic to create some additional matrices for these calculations. I will explain during the meeting.
Rebuild U matrix by adding process input values multiplied with price and scaled to one year in the [m+1]th column of the use matrix by matching NAICS input flow codes with NAICS economy model codes. Additionally subtract the process inputs multiplied with price and scale to one year from the corresponding cell whose NAICS code matched with the process input flows. There are easy formulas that do that. All we need is a simple match logic to create some additional matrices for these calculations. I will explain during the meeting.
Similar changes to F and B matrix. Add values to m+1th cell from process level information.
The additional step that we are doing in this part is called disaggregation. It will be helpful if this is programmed as a separate module because it will be again used at intermediate steps in the model generation algorithm later.

## Slide 6: Ending the first part
Once these new matrices have been created, we can use the SPA code for performing the calculations and get SPA results.
This ends the first part of the calculations.
I guess a good place to pause would be here before moving on to the next part. So I expect to have the interface perform these calculations before moving forward. The results would look like this.
384
0.000028 384 zero order 0.002119
0.184706 22----248----384 second order 14.175505
0.124531 22----384 first order 9.557308
0.067894 248----384 first order 5.210662
0.055437 198----384 first order 4.254624
0.038931 249----384 first order 2.987814
0.031219 1----198----384 second order 2.395986
0.025648 22----249----384 second order 1.968412
0.023611 282----198----384 second order 1.812051
0.012216 22----248----248----384 third order 0.937549
0.011893 245----249----384 second order 0.912739
0.010717 22----1----198----384 third order 0.822482
0.010391 280----198----384 second order 0.797442
0.009290 22----198----384 second order 0.712948
0.005664 241----248----384 second order 0.434669
0.005214 280----249----384 second order 0.400165
0.005163 198----198----384 second order 0.396206
0.004916 245----245----249----384 third order 0.37726